## Slide 1: GPIO interruptions on Pi
Handle interruptions in Python
  What NOT to do when handling multiple interruptions and how to fix it
Handle interruption in C/C++
Stress test – How fast interruption can go
  In Python
  In C/C++

## Slide 2
pulse time
period (T)
frequency = 1/T
rest time
(it depends on the pulse time)
repeat
1 second (10 edges per second)
verification of number of edges
200ms
after the last edge
 | Pulse Time | Frequency | Python Counts Lost | Python Lost % | C++ Counts Lost | C++ Lost % | Python | C++
 | 8 ms | 62.5 Hz | 126 of 105660 | 0.11% | 4 of 105660 | 0.003% |  | 
 | 4 ms | 125 Hz | 398 of 105660 | 0.37% | 18 of 105660 | 0.017% |  | 
 | 2 ms | 250 Hz | 344 of 105660 | 0.32% | 12 of 105660 | 0.011% |  | 
 | 1 ms | 500 Hz | 366 of 105660 | 0.34% | 56 of 105660 | 0.053% |  | 
 | 0.5 ms | 1 KHz | Losses every cycle |  | 76 of 105660 | 0.071% |  | 
 | 0.25 ms | 2 KHz |  |  | 113 of 105660 | 0.106% |  | 
 | 0.125 ms | 4 KHz |  |  | 332 of 105660 | 0.313% |  | 
 | 0.0625 ms | 8 KHz |  |  | Losses every cycle |  |  |